## Slide 1: College of Human Ecology Polyform Art Installation Updated Site Selection and Site Development Guidelines

## Slide 2
College of Human Ecology
Jenny Sabin Studio & Sabin Design Lab
Polyform
Plan view
Elevation
34’
Notes: Polyform is an outdoor room bounded by 8’ high glass walls bisected by crossing paths that define 4 quadrants each containing a laser cut and folded metal installation.

## Slide 3
Project Location
34’
6’
Site Selection
Notes: 5 exterior sites evaluated by the Campus Planning Office: Garden/Reservoir intersection; Overlook Terrace; HEB Courtyard; Belkin Courtyard; East Paths

## Slide 4
Preliminary Site Development Guidelines
Access through and around installation
Security: Protection from vehicles, lighting
Maintenance provisions
Accommodate future construction activities
Reservoir Drive
Garden Avenue
MVR West
Notes: We selected the corner of Garden and Reservoir, and suggested these general guidelines last time we presented to this committee. However, Required fire access to west path until MVR West is fully sprinklered; therefore need to select a temporary site until MVR construction completed.

## Slide 5
Recommended Sites
Notes: Temporary site until renovations to MVR West completed

## Slide 6
Temporary Site Development Guidelines
3’ clear from building wall
13’ clear from Commons exit
4’ min. interior passage
Interior lighting integral to sculpture
No winter maintenance on interior
Anchorage on roof deck
Commons Exit
Terrace
Pedestrian Bridge
Human
Ecology
Building

## Slide 7
Temporary Site Location

## Slide 8
Permanent Site Development Guidelines
3’ min. setback from Reservoir Avenue curb
10’ clear on other sides
6’ min. interior passage align with walkways
Bollards along Reservoir Avenue and new crosswalk
Snowmelt system under installation
Reservoir Drive
Garden Avenue
MVR West
CCC Building

## Slide 9
Permanent Site Location

## Slide 10
Additional Site Development Guidelines
Engineering considerations for attachment / footing:
  Withstand environmental conditions (wind, snow, etc.)
  Accommodate human interaction, e.g. climbing;
  Accommodate underground utilities;
  Facilitate temporary removal for maintenance;
  Elevate structure to permit stormwater runoff and maintenance;
Lighting for installation to be located within footprint and comply with municipal Dark Sky guidelines;
Develop and install interpretive signage;
Permanent site will require municipal approval;

## Slide 11
Proposed Schedule - 2017
Engineering Design End of February
Cornell Approvals March
Building Permit March 31
Fabrication April – May
Installation June

## Slide 12
Questions & Discussion